## Slide 1: Introduction
Project goal was to analyze well data from the Alberta and BC geographic region to infer formation characteristics
First and third parts focused on aggregating data from well and pressure test lists
Second part required creating interactive software to process diagnostic fracture injection tests

## Slide 2: DFIT Overview
4 points from pressure over time injection plot:
  Start
  Breakdown
  ISIP
  Closure

## Slide 3: Automatic Point Selection
Start: minimum slope threshold
Breakdown: maximum pressure
ISIP: deviation from post-breakdown slope
Closure: time-pressure differentials

## Slide 4: Program Implementation

## Slide 5: DFIT Interaction
Snap to zoom and point picking

## Slide 6: DFIT Interaction (2)
Independent snap to zoom

## Slide 7: DFIT Interaction (3)
Custom ISIP

## Slide 8: Closure Point Selection Details
Based on local density outlier analysis
Eliminate points with extreme rolling variance based on moving window statistics then take max
Better experimental results than simple max value or polynomial interpolation

## Slide 9: Pore Pressure
With the 4 points from the first part of the program, pore pressure can be calculated

## Slide 10: Program Implementation (2)
Following user interaction with 4 DFIT points

## Slide 11: Pore Pressure Interaction
Global region selection for data filtering

## Slide 12: Pore Pressure Interaction (2)
Local region selection for data filtering

## Slide 13: Pore Pressure Interaction (3)
Manual intercept override

## Slide 14: Conclusion
Program successfully achieves its purpose of making DFIT analysis more efficient than alternative methods (Excel, etc.) through the use of software that scales to large datasets and custom ways of interacting with data
From a technical perspective the use of Python’s Matplotlib library is the largest roadblock to further development since it is not designed for interactivity
Other areas of improvement are automatic selections of ISIP and closure – selection parameters aren’t directly accessible through program UI and better approaches may be possible in general